## Slide 1: Practical work on NEMO Converting files
M. Fichaut

## Slide 2: From ASCII data to XML files
Collection
of
ASCII files
ODV
files
CDI summary
CSV file
SeaDataNet
CDI
MIKADO
XML
CDI files
summary_CDI_NEMO.xml
Delivered with NEMO
Coupling table
Coupling table
Export

## Slide 3: NEMO installation
Open the install_nemo_1.5.3_windows.zip file (on the desktop)
Unzip it
Double click on launcher_nemo.bat
Follow the installation procedure
Don’t forget to add the NEMO shortcut on your desktop

## Slide 4: Collection of ASCII files
Training data set
  6 CTDs raw files under
    SDN tools/Practical work for new users/data/input files
  ASCII files with measured parameters in column
  Measured parameters = Depth, Temperature, Salinity, Fluorescence and Dissolved oxygen

## Slide 5: First step : conversion to ODV with NEMO
Run NEMO to convert the files to ODV format.
Modify the settings of NEMO
  Default directories for data set to
    Practical work for the new users/data
  Default directories for data set to
    Practical work for the new users/models
  Enter your EDMO ID in the field below using the search function (right click)
Proceed the 4 steps of NEMO

## Slide 6: NEMO – File description
Choose the type of file (cruise directory, cruise file, …)
Browse your PC to input the data files directory
Once the file is open in NEMO, have a look to its content
Choose file type : Profile
Choose the output format : ODV, one unique file for all stations or One file per station
Enter the Station header information
  there is a specific character string at the end of each Station header : *END*
The Data termination indicator is EOF (End of file)
Validate the step when description is OK

## Slide 7: NEMO – Station description
Station number is given on line “**Station”
Data type is ‘CTD stations’
Time is U.T.
Latitude format is NDD MM.mm
Longitude format is NDDD.MM.mm
Bottom Depth is not available
Input all the mandatory fields : station number, time, date, latitude, longitude
Use the Test function to verify your input
Validate the step when description is OK

## Slide 8: NEMO – Data description (1)
Select the parameter list to use : P01 via P02
Add the parameters : P021 codes are
  Depth : AHGT, Temperature : TEMP, Salinity : PSAL, Fluorescence : FVLT, Dissolved oxygen : DOXY, Input the units of the parameters (for salinity, use Dimensionless)
  Add a text label to each parameter
Set Start and End positions for the parameters
Tell NEMO which code is the vertical reference

## Slide 9: NEMO – Data description (2)
Format is mandatory
  Describe the output format that you want
  %6.1f : means 6 digits total (decimal point included), 1 digit for decimal, f for float (decimal number)
  Use the contextual menu ‘Select the format’ for predefined format
Use the test fields to validate your input
Validate the step when description is OK
Save you model in the model directory

## Slide 10: File conversion
You will be asked to give :
A dataset reference (can be a cruise name, for example)
A name for the output file (all the stations in the same file) or name for the output directory (one station per file) in the Practical work for new users/output directory
Have a look to the output files
Drag and drop the ODV files in ODV to test their conformity

## Slide 11: Practical work on NEMO Generating CDI summary and coupling table
M. Fichaut

## Slide 12: From ASCII data to XML files
Collection
of
ASCII files
ODV
files
CDI summary
CSV file
SeaDataNet
CDI
MIKADO
XML
CDI files
summary_CDI_NEMO.xml
Delivered with NEMO
Coupling table
Coupling table
Export

## Slide 13: Creation of the CDI-SUMMARY and the coupling table
Input the information in NEMO SETTINGS
  Mapping
    Click in the box Generate mapping for SeaDataNet download Manager
  SeaDataNET CDI summary
    Unfold the SeaDataNet CDI Summary block
    Click in the box Generate SeaDataNet CDI summary
    Fulfill all the mandatory fields (in red), using right click for the Search function

## Slide 14: Run the file conversion
Same file than in the previous exercise
You will be asked to give :
A dataset reference (can be a cruise name, for example)
A name for the CDI summary file
A name for the output file (all the stations in the same file) or name for the output directory (one station per file)
An output directory prefix (for the coupling table). This prefix will be subtracted from the file name in the mapping table.
  For example if
  output file name = C:\username\NEMO\cruise_name\file_name
  and output directory prefix = C:\username\NEMO
  file name in the mapping table will be : cruise_name\file_name

## Slide 15: CDI summary file
Convert it to an EXCEL file (for future use by MIKADO)
  Open the CDI summary text file with EXCEL (field delimited by tabulations)
  Rename the folder into : STATION
  Save it under XLS or XLSX format, it will be used later on during the practical work on MIKADO

## Slide 16: Coupling table
Have a look at the coupling table
  Menu : Coupling_table>Edit
  It gives the link between the LOCAL_CDI_ID and the file in which the LOCAL_CDI_ID will be found by the download manager of SeaDataNet
  MODUS = 1 if the LOCAL_CDI_ID is in a mono-station file
  MODUS = 3 if the LOCAL_CDI_ID is in a multi-station file
  One LOCAL_CDI_ID and one format is unique in the coupling table
  Add and delete records
Export the coupling table in a flat file
  Menu : Coupling_table>Export
  Have a look at the flat coupling.txt file

## Slide 17: Practical work on MIKADO Creation of XML files for CDI
M. Fichaut

## Slide 18: Exercise
CDI Automatic generation from the CDI summary file created this morning with NEMO – Validation of the XML files

## Slide 19: From ASCII data to XML files
Collection
of
ASCII files
ODV
files
CDI summary
CSV file
SeaDataNet
CDI
MIKADO
XML
CDI files
summary_CDI_NEMO.xml
Delivered with NEMO
Coupling table
Coupling table
Export
Coupling file for DM
a
b

## Slide 20: a) Configuration file for CDI XML
Run MIKADO
Open the configuration file delivered with NEMO :
  MIKADO => Automatic/Open/CDI
  the configuration file is in the HOME_DIRECTORY of NEMO, but for the training it is under \Practical work for new users\config , file summary_CDI_NEMO.xml
Make the connection with the Excel file that you have created with NEMO (the Excel file must be closed to avoid conflict access)
Check the connection (you must have a green message)
Go to the Queries tag and have a look at the queries
Check them (green message after check all)
Save your configuration file

## Slide 21: b) XML file generation
Run Automatic/Generate/CDI
  Open the configuration file
  \Practical work for new users\config\summary_CDI_NEMO.xml
  Choose the export directory (where CDI XML files will be written)
  Choose the type of export file you want :
    XML files
    Zip file containing the XML files
    Both (XML and Zip)
Open one XML export file to have a look at it with MIKADO Manual>Open>File>CDI